Open Plantb0t
Revision A-2 (Complete Redesign)

# Planned Features
- WiFi enabled SOM with integratd USB programmer
- Gated power on board with timed re-enable for ultra-low-power sleep
  - Coin cell backup battery for the RTC
  - RTC on I²C-Bus for easy configuration and re-programming
- Exposed GPIO for user additions (6x)
- I²C-Bus on extention pins and around the board
- On-Board sensor packages for Humidity, Temperature, Light and Soil Moisture via measuring sticks
- Extention ports for additional sensor boards
  - 2x I²C extentions for smart extention boards (Plantb0t Sense+)
  - 2x Analogue inputs with constant current source and ground measurement
- Analogue Multiplexer with switching via I²C
- Variable Gain Amplifier with I²C controller
- 10-bit Analog to Digital Converter (ADC) on I²C
- Volage regulator for USB power and power extention pins
- Power Extention Pins (PEP) to add external power handling (Plantb0t Power+)
- Status LEDs for sensors, power, programming and board state
- Form factor 5x5cm, all SMD parts on 2-layer boards.
# Bill of Materials (BoM)

Type	Device Number	Datasheet Link
ESP-12 SOM	ESP8266MOD	...
I²C Real Time Clock	DS1307	http://www.farnell.com/datasheets/1647366.pdf
USB Programmer	EFM8UB10F8G	http://www.farnell.com/datasheets/1884509.pdf
Constant Current Source	PSSI2021SAY	http://www.farnell.com/datasheets/667515.pdf
I²C Variable Resistor	MCP4017	http://www.farnell.com/datasheets/388001.pdf
Analog MUX	74HC4051	http://www.farnell.com/datasheets/1645588.pdf
I²C 4-bit I/O Expander	PCA9536	http://www.farnell.com/datasheets/1874752.pdf
Voltage Regulator	LM2937IMP-3.3	http://www.farnell.com/datasheets/1997654.pdf
Red Status LED	KPT-3216EC	http://www.farnell.com/datasheets/2045822.pdf
RGB Status LED	SML-522MU8WT86	http://www.farnell.com/datasheets/1996295.pdf

# I²C Bus Devices
- ESP-12 (Master)
- 10-bit ADC
- Analogue 4 to 1 MUX
- Variable Gain Amplifier Controller
- Plantb0t Sense+ via I²C (2x)
- On-Board sensor package
- Real Time Clock programmer
- (Plantb0t Power+) Battery charging circuit
- …