Open Plantb0t
Revision A-2 (Complete Redesign)

# Planned Features
- WiFi enabled SOM with integratd USB programmer
- Gated power on board with timed re-enable for ultra-low-power sleep
  - ATTiny10 powered via permanent power-on as power magement MCU
  - MCU on I²C-Bus for easy configuration and re-programming
- Exposed GPIO for user additions (7x)
- I²C-Bus on extention pins and around the board
- On-Board sensor packages for Humidity, Temperature, Light and Soil Moisture via measuring sticks
- Extention ports for additional sensor boards
  - 2x I²C extentions for smart extention boards (Plantb0t Sense+)
  - 4x Analogue inputs with constant current source and ground measurement
- Analogue Multiplexer with switching via I²C
- Variable Gain Amplifier with I²C controller
- Volage regulator for USB power and power extention pins
- Power Extention Pins (PEP) to add external power handling (Plantb0t Power+)
- Status LEDs for sensors, power, programming and board state
- Form factor 5x5cm, all SMD parts on 2-layer boards.
# I²C Bus Devices
- ESP-12 (Master)
- GPIO-Expander (8 channel)
- Variable Gain Amplifier Controller
- Plantb0t Sense+ via I²C (2x)
- On-Board sensor package
- ATTiny power management controller (PMC)
- …